Introduction

An operating system (OS) is system software that manages computer hardware and software resources and provides common services for computer programs. All computer programs, excluding firmware, require an operating system to function.
The components of an operating system all exist in order to make the different parts of a computer work together. All user software needs to go through the operating system in order to use any of the hardware, whether it be as simple as a mouse or keyboard or as complex as an Internet component.
## Components of an OS
### Kernel
With the aid of the firmware and device drivers, the kernel provides the most basic level of control over all of the computer's hardware devices. It manages memory access for programs in the RAM, it determines which programs get access to which hardware resources, it sets up or resets the CPU's operating states for optimal operation at all times, and it organizes the data for long-term non-volatile storage with file systems on such media as disks, tapes, flash memory, etc.
### Intruupts
Interrupts are central to operating systems, as they provide an efficient way for the operating system to interact with and react to its environment. The alternative – having the operating system "watch" the various sources of input for events (polling) that require action – can be found in older systems with very small stacks (50 or 60 bytes) but is unusual in modern systems with large stacks. Interrupt-based programming is directly supported by most modern CPUs. Interrupts provide a computer with a way of automatically saving local register contexts, and running specific code in response to events. Even very basic computers support hardware interrupts, and allow the programmer to specify code which may be run when that event takes place.
### Modes
Modern microprocessors (CPU or MPU) support multiple modes of operation. CPUs with this capability offer at least two modes: user mode and supervisor mode. In general terms, supervisor mode operation allows unrestricted access to all machine resources, including all MPU instructions. User mode operation sets limits on instruction use and typically disallows direct access to machine resources. At power-on or reset, the system begins in supervisor mode. Once an operating system kernel has been loaded and started, the boundary between user mode and supervisor mode (also known as kernel mode) can be established.
Supervisor mode is used by the kernel for low level tasks that need unrestricted access to hardware, such as controlling how memory is accessed, and communicating with devices such as disk drives and video display devices. User mode, in contrast, is used for almost everything else.

Privilege rings for the x86 microprocessor architecture available in protected mode.
## Booting the Operating System

 The Instruction Pointer (EIP) register holds the memory address for the instruction being executed by the processor. EIP is hardcoded to the value 0xFFFFFFF0. Thus, the x86 CPU is hardwired to begin execution at the physical address 0xFFFFFFF0. It is in fact, the last 16 bytes of the 32-bit address space. This memory address is called reset vector. The address 0xFFFFFFF0 will contain just a jump instruction to the address in memory where BIOS has copied itself.
Thus, the BIOS code starts its execution. BIOS first searches for a bootable device in the configured boot device order. It checks for a certain magic number to determine if the device is bootable or not. (whether bytes 511 and 512 of first sector are 0xAA55).
Once the BIOS has found a bootable device, it copies the contents of the device’s first sector into RAM starting from physical address 0x7c00; and then jumps into the address and executes the code just loaded. This code is called the bootloader.
The bootloader then loads the kernel at the physical address 0x100000. The address 0x100000 is used as the start-address for all big kernels on x86 machines.

All x86 processors begin in a simplistic 16-bit mode called real mode. The GRUB bootloader makes the switch to 32-bit protected mode by setting the lowest bit of CR0 register to 1. Thus the kernel loads in 32-bit protected mode.

When the PC is powered on, the system BIOS ROM takes control. When it is ready to start an OS, it has no idea how to do it. Because of this, it runs another program - the Boot Loader to load an OS. The BIOS does not at all know what internal format this program file is or what it does. Because of this, it treats the Boot Loader as a flat binary program. It loads whatever is on the Boot Sector of the Boot Disk and "jumps" to the first byte of that program file.

Because of this, the first part of the boot loader, also called the Boot Code or Stage 1 cannot be in C. This is because all C compilers output a program file that has a special internal format - they can be library files, object files, or executable files. There is only one language that natively supports this - assembly language.

Bootstrap Assembly
We like to write everything in C, but we cannot avoid a little bit of assembly. We will write a small file in x86 assembly-language that serves as the starting point for our kernel. All our assembly file will do is invoke an external function which we will write in C, and then halt the program flow.
## The entry point using assembly

The first task we will deal with is how the bootloader starts the kernel. We are lucky because there exists a Multiboot Standard, which describes an easy interface between the bootloader and the operating system kernel. It works by putting a few magic values in some global variables (known as a multiboot header), which is searched for by the bootloader. When it sees these values, it recognizes the kernel as multiboot compatible and it knows how to load us, and it can even forward us important information such as memory maps, but we won't need that yet.
section .text
    ;multiboot specifications i.e multiboot header
    align 4	/* align loaded modules on page boundaries */
    dd 0x1BADB002 /* 'magic number' lets bootloader find the header */
    dd 0x00 ;flags
    dd - (0x1BADB002 + 0x00) /* checksum of above, to prove we are multiboot */

Declare a multiboot header that marks the program as a kernel. These are magic values that are documented in the multiboot standard. The bootloader willsearch for this signature in the first 8 KiB of the kernel file, aligned at a 32-bit boundary. The signature is in its own section so the header can be forced to be within the first 8 KiB of the kernel file.

section .bss
resb 8192 ; 8KB for stack
stack_space:

The multiboot standard does not define the value of the stack pointer register (esp) and it is up to the kernel to provide a stack. This allocates room for a small stack by creating a symbol at the bottom of it, then allocating 8192 bytes for it, and finally creating a symbol at the top. The stack grows downwards on x86.
## How do we make sure that this assembly code will serve as the starting point of the kernel?

We will use a linker script that links the object files to produce the final kernel executable. (more explained later) In this linker script, we will explicitly specify that we want our binary to be loaded at the address 0x100000. This address, as I have said earlier, is where the kernel is expected to be. Thus, the bootloader will take care of firing the kernel’s entry point.
/*
* linker.ld
*/
OUTPUT_FORMAT(elf32-i386)
ENTRY(start)
SECTIONS
 {
   . = 0x100000;
   .text : { *(.text) }
   .data : { *(.data) }
   .bss : { *(.bss) }
 }
First, we set the output format of our output executable to be 32 bit Executable and Linkable Format (ELF). ELF is the standard binary file format for Unix-like systems on x86 architecture.
ENTRY takes one argument. It specifies the symbol name that should be the entry point of our executable.
SECTIONS is the most important part for us. Here, we define the layout of our executable. We could specify how the different sections are to be merged and at what location each of these is to be placed.
Within the braces that follow the SECTIONS statement, the period character (.) represents the location counter. The location counter is always initialized to 0x0 at beginning of the SECTIONS block. It can be modified by assigning a new value to it.
Remember, earlier I told you that kernel’s code should start at the address 0x100000. So, we set the location counter to 0x100000.
The asterisk (*) is a wildcard character that matches any file name. The expression *(.text) thus means all .text input sections from all input files.
So, the linker merges all text sections of the object files to the executable’s text section, at the address stored in the location counter. Thus, the code section of our executable begins at 0x100000.
After the linker places the text output section, the value of the location counter will become 0x1000000 + the size of the text output section.
Similarly, the data and bss sections are merged and placed at the then values of location-counter.
Kernel

In order to understand what an OS Kernel is, we need to first understand what a "kernel" is at it's basic definitions. Dictionaries define "kernel" as "core", "essental part", or even "The body of something". When applying this definition to an Operating System envirement, we can easily state that:
The Kernel is the core component of an operating system.
## Basic VGA Driver Support

The most used VGA video mode for a text UI is "VGA mode 3". This is the most commonly used, as it allows direct memory access to a linear address containing each character and it's associated attributes. VGA mode 3 provides a text interface 80 characters wide and 25 characters lines per screen.
In VGA mode 3, the linear text buffer is located in physical at 0xB8000. Reading and writing to and from this address will provide direct manipulation of on screen text. To access a particular character on the screen from X and Y coordinates is simple using the following formula:
position = (y_position * characters_per_line) + x_position;

Each character takes up two bytes of space in memory. The first byte is split into two segments, the forecolour, and the backcolour. The second byte is a n 8-bit ASCII value of the character to print.

Bit 76543210
    ||||||||
    |||||^^^-fore colour
    ||||^----fore colour bright bit
    |^^^-----back colour
    ^--------back colour bright bit OR enables blinking Text

15 12 11 8 7 0 / Backcolor Forecolor Character

The following C code initializes the VGA memory buffer and prints ‘blank spaces’ i.e to clear the entire screen.

void terminal_initialize(void) {
        terminal_row = 0;
        terminal_column = 0;
        terminal_color = vga_entry_color(VGA_COLOR_LIGHT_GREY, VGA_COLOR_BLACK);
        terminal_buffer = (uint16_t*) 0xB8000;
        for (size_t y = 0; y < VGA_HEIGHT; y++) {
        for (size_t x = 0; x < VGA_WIDTH; x++) {
        const size_t index = y * VGA_WIDTH + x;
        terminal_buffer[index] = vga_entry(' ', terminal_color);
        }
        }
}

To print a character onto the screen. We need to copy the character to the current cursor position in the linear buffer. Since each character is represented by 2 bytes, we will need to set the foreground and background color as well. The following code does so.
void terminal_putentryat(char c, uint8_t color, size_t x, size_t y) {
        const size_t index = y * VGA_WIDTH + x;
        terminal_buffer[index] = vga_entry(c, color);
}
void terminal_putchar(char c) {
        terminal_putentryat(c, terminal_color, terminal_column, terminal_row);
        if (++terminal_column == VGA_WIDTH) {
        terminal_column = 0;
        if (++terminal_row == VGA_HEIGHT)
        terminal_row = 0;
        }
}
void terminal_writestring(const char* data) {
        terminal_write(data, strlen(data));
}
/* this is the basic kernel call with only the vga support */
void kernel_main(void) {

        terminal_initialize();

        terminal_writestring("Hello, kernel World!\n");
}

In the bootloader we call kernel_main() to handover the control to our kernel.
extern main_kernel
extern keyboard_handler_main
start:
    cli ;block all interrupts
    mov esp, stack_space
    call main_kernel
    hlt

I/O Sub-system

We communicate with I/O devices using I/O ports. These ports are just specific address on the x86’s I/O bus, nothing more. The read/write operations from these ports are accomplished using specific instructions built into the processor.
In read_port, the port number is taken as argument. When compiler calls your function, it pushes all its arguments onto the stack. The argument is copied to the register edx using the stack pointer. The register dx is the lower 16 bits of edx. The in instruction here reads the port whose number is given by dx and puts the result in al. Register al is the lower 8 bits of eax. If you remember your college lessons, function return values are received through the eax register. Thus read_port lets us read I/O ports.
read_port:
        mov edx, [esp + 4]
        in al, dx
        ret

write_port:
        mov edx, [esp + 4]
        mov al, [esp + 4 + 4]
        out dx, al
        ret
write_port is very similar. Here we take 2 arguments: port number and the data to be written. The out instruction writes the data to the port.
## Interrupts
We need to understand how the processor gets to know that the device has performed an event.
The easiest solution is polling - to keep checking the status of the device forever. This, for obvious reasons is not efficient and practical. This is where interrupts come into the picture. An interrupt is a signal sent to the processor by the hardware or software indicating an event. With interrupts, we can avoid polling and act only when the specific interrupt we are interested in is triggered.
A device or a chip called Programmable Interrupt Controller (PIC) is responsible for x86 being an interrupt driven architecture. It manages hardware interrupts and sends them to the appropriate system interrupt.

When certain actions are performed on a hardware device, it sends a pulse called Interrupt Request (IRQ) along its specific interrupt line to the PIC chip. The PIC then translates the received IRQ into a system interrupt, and sends a message to interrupt the CPU from whatever it is doing. It is then the kernel’s job to handle these interrupts.
## Keyboard

The keyboard works through the I/O ports 0x60 and 0x64. Port 0x60 gives the data (pressed key) and port 0x64 gives the status. However, you have to know exactly when to read these ports.
Interrupts come quite handy here. When a key is pressed, the keyboard gives a signal to the PIC along its interrupt line IRQ1. The PIC has an offset value stored during initialization of the PIC. It adds the input line number to this offset to form the Interrupt number. Then the processor looks up a certain data structure called the Interrupt Descriptor Table (IDT) to give the interrupt handler address corresponding to the interrupt number.
Interrupt Descriptor Table
An IDT(Interrupt Descriptor Table) is an array of descriptors(each 8 bytes long) that is used to associate interrupts and exceptions with ISRs. The IDT can hold a maximum of 256 descriptors(as there are 256 interrupts total on the PC). You are not required to have an IDT with a full 256 descriptors in it, just enough descriptors for the interrupts you are going to use. We tell the CPU where the IDT is via the LIDT assembly instruction.

31	15	14	12	7	4	0
Offset 31-16(word)	Present(1 bit)	DPL(2 bits)	01110(5 bits)	000(3 bits)	Not Used	4
Selector31-16(word)	Offset 15-0(word)					0

The following code sets up the IDT structure in our OS.
struct IDT_entry{
        unsigned short int offset_lowerbits;
        unsigned short int selector;
        unsigned char zero;
        unsigned char type_attr;
        unsigned short int offset_higherbits;
};
- Base is a 32 bit value split between bits 16-39 and bits 56-63 of the descriptor.
- Limit is a 20 bit value split between bits 0-15 and bits 48-51 of the descriptor.
- Offset is a 32 bit values split between bits 0-15 and bits 48-63 of the descriptor.
- Selector is a 16 bit value in bits 16-31 of the descriptor.
- Attributes are a collection of values in bits 32-47 of a gate or in bits 40-47 plus 52-55 of a nongate.
Modern x86 systems have 2 PIC chips each having 8 input lines. Let’s call them PIC1 and PIC2. PIC1 receives IRQ0 to IRQ7 and PIC2 receives IRQ8 to IRQ15. PIC1 uses port 0x20 for Command and 0x21 for Data. PIC2 uses port 0xA0 for Command and 0xA1 for Data.
/* Ports
        *	PIC1	PIC2
        *Command	0x20	0xA0
        *Data	0x21	0xA1
        */

The PICs are initialized using 8-bit command words known as Initialization command words (ICW). See this link for the exact bit-by-bit syntax of these commands.
In protected mode, the first command you will need to give the two PICs is the initialize command ICW1 (0x11). This command makes the PIC wait for 3 more initialization words on the data port.
These commands tell the PICs about:
- Its vector offset. (ICW2)
- How the PICs wired as master/slaves. (ICW3).
- Gives additional information about the environment. (ICW4)
Each PIC has an internal 8 bit register named Interrupt Mask Register (IMR). This register stores a bitmap of the IRQ lines going into the PIC. When a bit is set, the PIC ignores the request. This means we can enable and disable the nth IRQ line by making the value of the nth bit in the IMR as 0 and 1 respectively. Reading from the data port returns value in the IMR register, and writing to it sets the register. Here in our code, after initializing the PICs; we set all bits to 1 thereby disabling all IRQ lines.
 Now, we need to populate the IDT such that the interrupt number for the keyboard is mapped to the address of the keyboard handler function we will write.
The keyboard uses IRQ1. This is the input line 1 of PIC1. We have initialized PIC1 to an offset 0x20 (see ICW2). To find interrupt number, add 1 + 0x20 ie. 0x21. So, keyboard handler address has to be mapped against interrupt 0x21 in the IDT.
        /* populate IDT entry of keyboard's interrupt */
        keyboard_address = (unsigned long)keyboard_handler;
        IDT[0x21].offset_lowerbits = keyboard_address & 0xffff;
        IDT[0x21].selector = 0x08; /* KERNEL_CODE_SEGMENT_OFFSET */
        IDT[0x21].zero = 0;
        IDT[0x21].type_attr = 0x8e; /* INTERRUPT_GATE */
        IDT[0x21].offset_higherbits = (keyboard_address & 0xffff0000) >> 16;
Each IDT entry consist of 64 bits. In the IDT entry for the interrupt, we do not store the entire address of the handler function together. We split it into 2 parts of 16 bits. The lower bits are stored in the first 16 bits of the IDT entry and the higher 16 bits are stored in the last 16 bits of the IDT entry. This is done to maintain compatibility with the 286.
In the IDT entry, we also have to set the type - that this is done to trap an interrupt. We also need to give the kernel code segment offset. GRUB bootloader sets up a GDT for us. Each GDT entry is 8 bytes long, and the kernel code descriptor is the second segment; so its offset is 0x08 .
Interrupt gate is represented by 0x8e. The remaining 8 bits in the middle has to be filled with all zeroes. In this way, we have filled the IDT entry corresponding to the keyboard’s interrupt.

load_idt:
    mov edx,[esp+4]
    lidt [edx]
    sti
    ret

Once the required mappings are done in the IDT, we got to tell the CPU where the IDT is located.
This is done via the lidt assembly instruction. lidt take one operand. The operand must be a pointer to a descriptor structure that describes the IDT.

We first signal EOI (End Of Interrput acknowlegment) by writing it to the PIC’s command port. Only after this; will the PIC allow further interrupt requests. We have to read 2 ports here - the data port 0x60 and the command/status port 0x64.

void keyboard_handler_main(void)
{
    unsigned char status;
    char keycode;

    /* write EOI */
    write_to_port(0x20, 0x20);

    status = read_from_port(0x64);
    /* Lowest bit of status will be set if buffer is not empty */
    if (status & 0x01)
    {
        keycode = read_from_port(0x60);
        if (keycode < 0)
        return;

        if (keycode == ENTER_KEY_CODE)
        {
        //kprint_newline();

        terminal_putchar('\n');
        //terminal_writestring(command);
        //terminal_putchar('\n');
        command_ptr = 0;
        if (str_compare(command, "") == 1)
        {
        terminal_writestring("empty\n");
        terminal_writestring(generate_prompt());
        terminal_writestring(PROMPT);
        clear_str(command, '\0', strlen(command));
        return;
        }
        //terminal_writestring(command);

        //terminal_putchar('\n');
        process_command(command);
        clear_str(command, '\0', strlen(command));
        terminal_writestring(generate_prompt());
        terminal_writestring(PROMPT);
        clear_str(command, '\0', strlen(command));
        return;
        }
        if (keycode == 0x4B)
        {
        terminal_col -= 1;
        terminal_move_cursor();
        return;
        }
        if (keycode == 0x4D)
        {
        terminal_col += 1;
        terminal_move_cursor();
        return;
        }
        //terminal_putchar(current);
        char current = kmap[(unsigned long)keycode];
        terminal_putchar(current);
        if (current != '\b')
        command[command_ptr++] = current;
        else
        command_ptr--;
    }
}

We first read port 0x64 to get the status. If the lowest bit of the status is 0, it means the buffer is empty and there is no data to read. In other cases, we can read the data port 0x60. This port will give us a keycode of the key pressed. Each keycode corresponds to each key on the keyboard. We use a simple character array defined in the file kmap.h to map the keycode to the corresponding character.